## Slide 1: OSI Security Model
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 2: The OSI Layers
OSI Security Model

## Slide 3: The OSI Layers
Open System Interconnection or OSI layers
Reference model for how information from software in one device moves to an application on another computer
Copyright © 2021 by Elephant Scale, All Rights Reserved
Notes: Image credit: https://superuser.com/questions/874393/what-protocol-is-used-to-transfer-a-message-in-a-http-application
Licensed for free use and sharing with attribution and without modification

## Slide 4: The OSI Layers
Maps to various implementations
TCP/IP architecture for example
Copyright © 2021 by Elephant Scale, All Rights Reserved
Notes: Image Credit: https://nicolaswindpassinger.com/osi-reference-model

## Slide 5: The OSI and IoT
OSI maps to different protocols and standards for web and IoT worlds
Copyright © 2021 by Elephant Scale, All Rights Reserved
Notes: Image Credit: https://nicolaswindpassinger.com/osi-reference-model

## Slide 6: Application Layer
Represents processes on the level of applications and users, IoT and otherwise
Links the business application access to network services
Messaging protocols found at this layer CoAP, MQTT, XMPP, AMPQP and HTTP
Notes: Ref:

## Slide 7: Presentation Layer
Formats and encrypts data for communication.
Resolves compatibility issues in the communication between the application and the network.
For example, TLS class of cryptographic protocols
Notes: Ref:

## Slide 8: Session Layer
Connections between local and remote applications are initiated, managed and terminated here
Manages sessions over multiple devices on the same network
Notes: Ref:

## Slide 9: Transport Layer
Manages the host-to-host data transmission
Ensures that data transfers between hosts are completed.
Manages error recovery and retransmission of lost data.
TCP and UDP are two common protocols in this layer
Notes: Ref:

## Slide 10: Network Layer
Responsible for routing and transferring data packets between different nodes across various networks
Includes the IP the Internet Protocol part of TCP/IP
Of concern to IoT is that it also includes IPv4 and IPv6
Notes: Ref:

## Slide 11: Data Link Layer
Later where data transfer between two directly connected nodes in a network takes place
Divided into two sub layers:
  Medium access control layer (MAC layer)
  Logical link control layer (LLC).
Various IEEE 802 standards apply to this layer
  IEEE 802.15.4 or low rate Wireless PAN for example
Notes: Ref:

## Slide 12: Physical Layer
Layer where networks are organized
Foundation of IoT and its connected
Includes the essential physical structure needed to make the IoT possible
  E.g., cables and radio frequency links
  Essential transmission specifications, communication protocols and hardware on a device and data level.=
Notes: Ref:

## Slide 13: OST Intuitive Model
Using OSI to figure out why an application isn’t working
  Layer 1: Physical
  Is the network cable plugged in?
  Layer 2: Data Link
  Do you have a link light?
  Layer 3: Network
  Are you getting an IP?
  Layer 4: Transport
  Can you connect to your default gateway?
  Layer 5: Session
  Do you have DNS server information?
  Can you ping 4.2.2.2 but not google.com?
  Layers 6&7: Presentation & Application –
  Can you browse to a site?

## Slide 14: Common Attacks by Layer
OSI Security Model

## Slide 15: Examples of Attacks at Each Level
Layer | Description | Attack
7 | Application | Social Engineering, UserID/Password sniffing. Lack of role-based security for admin and support. Spoofing authentication credentials
6 | Presentation | Phishing, TLS/SSL sniffing Breaking weak or faulty encryption
5 | Session | Hacking – Telnet and FTP hacking Access to unsecured applications
4 | Transport | TCP Sessions sniffing Port sniffing
3 | Network | Man in the Middle Attacks Port sniffing
2 | Data Link | Spoofing MAC/ARP sniffing
1 | Physical | Sniffing, physical device compromise

## Slide 16: Application Level Security
Refers to the applications that support the end user functions
  Applications at this layer include FTP, SMTP and other services
  Supports user applications with that authentication and authorization
Main security challenge for IIoT is unauthorized access to control systems
  Entry point to introduce additional vectors – e.g, creating backdoors for future attacks
  Common attack vector using social engineering, phishing and other deceptive exploits
First line of defense is strong organizational procedures and policies on issuing, revoking and changing authentication credentials

## Slide 17: Application Level Security
UserID/Password is common authentication
  Often implemented with weak account policy
  Users suffer from password fatigue
    Tend to use the same password across accounts
    Tend to use short easy to guess passwords
    Tend to not change their passwords
Mitigations
  Password policy requiring strong passwords and regular rotations
  Use generated tokens instead of passwords
    These have higher entropy and are harder to crack
    Eliminates the problem of password reuse
  MFA – multi-factor authentication
    Requires authentication from two of three possible sources
      What the user knows – password or token
      Where the user is – specific IP address
      Something the user has – mobile phone for a confirmation code
Notes: Several attacks have been documented where an individual used the same password for an administration account as they did for a social media account. The credentials were hacked from the social media account and then used to access the corporate network.

## Slide 18: Presentation Level Security
Encryption is performed at this layer
Common attacks often involve weak or missing encryption
  There must be both encryption for data in transit and encryption for data at rest
Exploitable weaknesses can occur when:
  An encryption standard is used that is too weak, one that has known weaknesses for example
  Flawed implementation of the encryption such as:
    Keys are too short
    Salts are not used in digests allowing the use of rainbow tables to reverse engineer passwords
    Using an encryption library that has not been fully vetted
    Using a home-grown encryption library that is not full tested
  Flawed application of an encryption application
    Failure to encrypt data when it should be
    Not encrypting some data that is accessible

## Slide 19: Presentation Level Security
Presentation level security can be subverted at the application level
Called a Man in the Browser (MiTB) attack
  Access is gained at the application level to steal or alter data before it become encrypted
Often the result of human engineering
  Compromised user installs malware
  Or malware is installed from a phishing or other attack
Can be mitigated to a degree by isolation
  Applications used for systems control do not have access to other applications
  No public access to the user control apps
  Only the absolute minimum network access to private networks
Ideally, control systems only connect to the system they control

## Slide 20: Man in the Browser

## Slide 21: Session Level Security
The main attacks at this level deal with interfering with sessions or some sort of session hijack
Man in the Middle (MiTD) attacks occur when an adversary can intercept communications between two parties in a session
A main risk is that an adversary could take over an automated system by hijacking a session between the system and an operator
Some potential exploits
  Failure to use regular confirmation of identity of participant
    Ignoring warning about expired TSL certificate for example
  Failure to rotate credentials during a session
    The longer a set of credentials is used, the more likely they are to be hacked
  Failure to securely transmit session information
    Often makes the session tokens or ids guessable by an adversary

## Slide 22: Transport Level Security
Internet based attacks probe for open ports
  Can be used to inject malware
  Malware often opens other ports as a backdoor
Mitigations involve
  Regular port scans
  Use of non-standard ports to confound probing for commonly used ports
  Firewalls to block access to most ports except those explicitly allowed on a whitelist
Known or published IP addresses are potential targets
Mitigations involve
  Use of an API gateway to map external IP addresses to internal addresses
  Use of filtering and firewalling on the gateway
  Establishment of a DNZ

## Slide 23: Demilitarized Zone and Honey Pots
  DMZs connect internal networks to the outside world
    Internal networks cannot be accessed directly
    Must go through the DMZ
    Including standard application-level attacks
  Honeypots are fake networks
    Designed to distract attackers
    They wind up attacking the honeypot instead of the industrial system

## Slide 24: Network Layer Security
Level at which most network hardware operates
  Switches, routers, firewalls, etc.
Attacker can reroute traffic via a compromised router
  Many commercial routers have security flaws
Malware insertion into network devices is a common attack
  Used by the NSA as part of their Tailored Access Operations (TAO)
  Network devices are physically intercepted during shipment
  Malware is installed to create backdoors
Security analyses often overlook off the shelf hardware

## Slide 25: ARP Spoofing Attack

## Slide 26: Network Layer Security
Mitigations involve
  Using NAT and other address translation strategies
  Physically secure network equipment
  Breeches at this layer commonly occur inside the organization
  The use of VPNs where possible
  However, this does add a layer of latency and complexity
  Full security audits of all network equipment

## Slide 27: Data Link Layer Security
This layer works on the MAC address and packet layer
Common attack is to force a Network Interface Controller (NIC) into promiscuous mode
  This allows it to absorb traffic intended for other machines
This is also the layer where attackers may spoof a MAC address
Mitigation
  A common mitigation is to create separate virtual LANS (VLANs) on a single physical LAN
  Access control lists can then be applied to the different VLANs
  Disabling unused ports also helps at this layer too

## Slide 28: Physical Layer Security
Most common attack is compromised physical devices
  Access to the devices creates opportunities for insertion of malware or physical taps or attacks
First line of defense
  Physically isolate and lock up all the equipment
  Allow access only to vetted people who need access
  Use the lowest level of access needed
Social engineering attacks try to convince staff to allow access to bad actors
  Mitigation is to have strongly enforced security measures
  “We will not open the server room for anyone who claims to have lost their keycard.”
Physical interception is done by accessing cables and other devices – data taps for example
  Also done by monitoring EM signals from monitors and other devices

## Slide 29: Physical Layer Security
Common vector to disable physical devices
  Power overloads
  EM pulses or physical damage
Mitigations
  Any device, cable or other “thing” connected to the network is vulnerable
  Use proper shielding and physical isolation when necessary
  Have a good disaster recover plan for loss of physical assets

## Slide 30: Defense in Depth
OSI Security Model

## Slide 31: Defense in Depth
Any IoT security solution must include a security model and plan for each of the OSI levels or their equivalent
Any deployed system is as insecure as the security at its weakest level

## Slide 32: OSI mitigations

## Slide 33: Layer One Attacks
Traditional cybersecurity improvements push attackers toward alternative paths
  The physical layer has become a fertile ground for attacks
  Effectively, the soft underbelly of cybersecurity
Can take the form of a compromised employee planting a device on the network
Rogue and insecure hardware is often missed during security audits
  Legitimate hardware can be altered to provide insecure access
Zero-trust network security causes attackers to look at physical access via hardware exploits
  Even air-gapping is not an effective solution
  For example, STUXNET
Notes: Taken from https://www.helpnetsecurity.com/2021/09/14/osi-layer-1/

## Slide 34: Hardware Security Challenges
Firmware can be updated with compromised versions
  Often overlooked in security testing
Recommended mitigation
  automated security validation tools that can scan for configuration anomalies within their platform and evaluate security-sensitive bits within their firmware
Hardware uses multiple components from different manufacturers, each using a different supply chain
  Security has to be enforced across the supply chain
Problem made more urgent by the increased use of systems on chips (SoCs)
  SoCs consolidate multiple traditional components on a single chip
  Bypasses the more traditional network security analysis
Notes: Taken from https://www.helpnetsecurity.com/2021/09/14/osi-layer-1/