## Slide 1: Security Design
Security Design
Security Design
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 2: Secure by Design
Securing the IIoT does not require radically new ideas, concepts or techniques
Instead, existing best practices in all areas of IT security need to be updated and integrated
Starting point is the concept of secure by design
  Ensures that security is a primary objective at all stages of product creation and deployment
  Avoids security being “added on” after development
  Remedial security is historically the source of many breeches
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 3: Secure by Design
The problem faced is:
  IoT is still in its early stages
  Need to extend and integrate cyber security and physical security for cyber-physical systems
Three main principles
  Threat analysis: starts with a security threat analysis
  Defense in depth: full stack security design
  Security everywhere: no part of a system is ignored
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 4: IoT Security Blueprint
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 5: IoT Foundation Best Practices
Classification of Data
Physical Security
Device Secure Boot
Secure Operating System
Application Security
Credential Management
Encryption
Network Connections
Secure Software Updates
Logging
Software Update Policy
Assessing a Secure Boot Process
Software Image and Update
Side Channel Attacks
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 6: Classification of Data
Define a data classification scheme and document it
  Defines classes or levels of sensitivity for data
  Ensures right level of security is implemented
  Ensures compliance with legal regulations
Assess every item of data stored, processed, transmitted or received by a device
  Apply a data classification rating to each item
  Collections of data may be more sensitive than individual items and may be classified differently
Ensure the security design protects every data item and collections of items against unauthorized viewing, changing or deletion, to at least its classification rating or higher
When documenting the security design, also document the data items, their classification and the security design features that protect them
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 7: Physical Security
IoT devices are often deployed in easily accessible locations
  Increases risk of physical damage, tampering with switches and making connections to management, debugging and test ports
Secure devices by physically barring access and removing all means of unwanted connection
Any interface used for administration or test purposes during development should be removed from a production device, disabled or made physically inaccessible
All test access points on production units must be disabled or locked
Necessary administration ports must have effective access controls
  Strong credential management,
  Restricted ports
  Secure protocols etc.
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 8: Physical Security
Device circuitry should physically inaccessible to tampering
  e.g. epoxy chips to circuit board, resin encapsulation, hiding data and address lines under these components etc.
Secure protective casing and mounting options for deployment of devices in exposed locations
To identify possible problems in the supply chain, make the device and packaging “tamper evident”
Shield against side-channel attacks
  E.g. monitoring of power consumption or temperature
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 9: Device Secure Boot
Uses a staged boot sequence to minimize risk
  Every stage is checked for validity before initializing
  Minimizes risk of rogue code being run at boot time
Ensure a ROM-based secure boot function is always used
Use a hardware-based tamper-resistant capability
  E.g. Secure Access Module (SAM) or Trusted Platform Module (TPM)
  Stores crucial data items and runs the trusted authentication and cryptographic functions required for the boot process.
  Must hold the read-only first stage of the bootloader and all other data required to verify the authenticity of firmware
Check each stage of boot code is valid and trusted immediately before execution
  Reduces the risk of TOCTOU attacks (Time of Check to Time of Use)
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 10: Device Secure Boot
At each stage check that only the expected hardware is present and matches the stage’s configuration parameters
Do not boot the next stage of device functionality until the previous stage has been successfully booted.
Ensure failures at any stage of the boot sequence fail gracefully into a secure state that prevents unauthorized access
This applies to the booting up a device, not software that runs of the device – that is covered later
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 11: Secure Operating System
The OS should have only the components that support the functioning of the device – everything else is removed
Should use the latest stable OS components
OS should use the most secure settings available
Apply secure boot principles (last section) to the OS
Disable all unused ports, protocols and services
Apply tested updates
Disable write access to the root file system for users and applications
Do not use “root” – create an administrator account that has only the rights needed for administering the device
Use an encrypted file system
Document the OS security configuration
Apply minimum access rights to all files and directories
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 12: Application Security
Document the security design of applications
Applications must have the lowest privilege level possible
Applications have access only to resources they need
Applications should be isolated from each other
Ensure applications were created with secure development principles – for example, secure code standards compliance
Ensure SDLC incorporate security into all phases of development, design and test
Use secure coding techniques as documented for that language
Ensure all errors and exceptions are handled securely
Ensure no hard coded credentials in the code
Ensure no secrets are recorded in errors or log files
Never deploy debug version of code
Plan for network connectivity loss to avoid insecure states
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 13: Credential Management
Device should be uniquely identifiable by means of a factory-set tamper resistant hardware identifier or equivalent
Use good password management techniques
Password credentials must use an industry standard hash function, along with a unique non-guessable salt value
All credentials must be strongly encrypted
Use a secure storage for credentials, e.g. Hashicorp Vault
Use multi-factor authentication wherever possible
Ensure a trusted time source is used for signing
Manage digital certificates carefully, including replacing certificates
  Certificates should be used to identify only one device
Factory resets should remove all data and stored credentials on a device
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 14: Encryption
Apply the level of encryption appropriate for that data classification
Use industry standard tools and the strongest and most recent version of algorithms
When connections allow a selection of different protocols, remove the weaker ones from the list of options
Do not use insecure protocols like HTTP or FTP
Store keys securely with a secrets manager
Ensure keys can be updated remotely and securely
Avoid using global keys
  Each device that uses encryption should have its own keys
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 15: Network Connections
Network access points are high risk points of attack
Activate only the network interfaces that are required
Run only the services on the network that are required
Open only ports that are required
Always use a correctly configured firewall
Always use secure protocols like HTTPS, SFTP
Never send or store credentials in plain text
Authenticate every inbound connection to ensure it is from a legitimate source
Authenticate the destination of any sensitive data before it is sent
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 16: Software Updates
Encrypt update packages to prevent tampering
Cryptographically validate the integrity and authenticity of a software update package before installation begins
Ensure that the package cannot be modified or replaced by an attacker between being validated and installed
  TOCTOU (Time of Check to Time of Use) attack
The installation must resolve and validate all required dependencies for the update
  If this fails, the system should be left in a secure and stable state
Unsure the system goes into a safe and secure state if the update fails
Institute anti-rollback to prevent attackers from reverting the software back to an earlier unsecure version
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 17: Logging
All logged data must comply with appropriate data protection regulations
Logging function runs in its own process
Log files are stored separate from operational and other files
Set maximum log file size and enable log file rotation
Minimum logging must include
  Start up and shut down parameters
  Access and login attempts
  Unexpected events
Restrict access rights to log files to the minimum required to function
If logging to a central repository, send log data over a secure channel to avoid eavesdropping or tampering
Monitor and analyze logs regularly to extract valuable information and insight
Synchronize to an accurate time source for accurate timestamps
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 18: Software Update Policy
Both system builders and users must have a policy about updating software on devices in the field including
  Management of all connected devices over their complete device lifecycle
  A clear, publicized, process for managing software errata
  Clearly defined mechanisms within the software architecture for software updates
  Conformance with standards for software patching
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 19: Secure Boot Process
The secure boot cannot be bypassed
All code loaded as part of the boot process, unless it runs directly from ROM, is verified to ensure:
  The code was created by the expected, authorized sources
  The code has not been modified since it was created
  The code is intended for the device type on which it is to be run
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 20: Secure Boot Process
Verify code after it has been loaded into RAM as opposed to before when it is in persistent storage
The boot sequence starts running from ROM, using an immutable root key to verify the first code to be loaded
Modules of code are loaded progressively, but only after each previous stage has been successfully verified and booted
Any existing data currently installed on the device that will be used as part of the boot configuration is checked for length, type, range etc. prior to use within the boot process
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 21: Secure Boot Process
At each stage of the boot process the boot software checks that the hardware configuration matches the expected configuration parameters for that stage
The boot process ensures that if an error occurs during any stage of the process, the device “fails gracefully” into a secure state in which RAM has been cleared of residual code
  Failed boots do not leave the device open to unauthorized access
Bootloader code is updated to address vulnerabilities
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 22: Software Image and Update
To establish the authenticity and integrity of a software update, a cryptographic signature is attached to the software package
  Devices only install updates if they first verify the signature
The signature’s cryptographic key size and hash algorithms have sufficient cryptographic strength for the intended service life of the product
The signature method chosen has a key provisioning method suitable for the intended manufacturing supply chain
The system makes use of any hardware cryptography support available on the device, such as hardware key store, accelerated hashing and decryption operations
The copies of the symmetric or asymmetric keys used to create the software component signatures are stored in sufficiently secure storage
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 23: Side Channel Attacks
A Side Channel is an unintended/unanticipated capability to observe changes in the state of a component
  Could be at the chip, board, application, device or network level
  Deduce information based on these changes and then use that information to exploit the system
  Especially when dealing with high-risk scenarios or those in harsh environments
Fault Injections deliberately runs a system under conditions outside those for which it was designed
  Can be used to establish side channels
Side channel mitigations
  Obfuscate signals by varying amplitude and/or time domain
  Randomize jitter and delay
  Obfuscate hardware and software-based functions with randomized performance regardless of the inputs
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 24: Side Channel Attacks
Side channel mitigations
  Insert dummy operations
  Design circuitry to fail gracefully and reliably as power supply rails reach designed limits
  Design circuitry to fail gracefully and reliably as temperature reaches designed limits
  Include fault injection countermeasures in the design
  Employ appropriate mitigating physical construction (mountings, housing, EMF shields etc.)
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 25: Security Design
Security Design Security Design
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 26: Secure Development
In addition to secure design of the product
The development process must also be secure
Removes opportunities for bad actors to subvert the development process
Also deals with securing the management, administrative and support functions during development
  We know that the test results have not been tampered with if we have a secure testing process.
Secure Ops also covers the operational processes to ensure they are defined with security in mind
  Cuts across all organizational units
This is one of the goals of DevSecOps
  Security doesn’t apply to what we do but how we do it as well
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 27: The Specification
A spec is a description of what is to be built, its capabilities and functionality
  All engineering projects are built to a specification
  Provides a baseline for testing and quality analysis
  Not a design - only describes what the deliverable should be
Designs describe how to build something from a spec with the resources and technology available to the development team
  One spec may give rise to multiple designs
  Designs are the phase where solutions to nonfunctional requirements are crafted
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 28: Why a Specification?
Poorly designed software is inherently insecure
We can't have well-designed software unless we know:
  Exactly what the software should do
  What the software must not do
  How the software should handle errors and exceptions
  How the software should respond to attacks
Since the spec describes exactly how the software will perform
  Testers start developing tests based on the specification
  Security testers also start developing penetration and exploit tests based on the spec
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 29: Securing the Development Process
Design process security prevents the insertion of malicious code during development
Three examples of malicious code insertion
  Backdoors: Programmers insert code that allows unauthorized access to the system
  Logic Bombs: Code designed to compromise or damage the system when triggered by an attacker
  Surprise Functionality: Functionality that is not in the spec that can be exploited by an attacker
Malicious code insertion is generally cannot be identified by standard testing
  White box testing that exercises all the code must also be employed
  Part of what testers do in exploratory testing is to look for surprise functionality
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 30: Logic Bomb Examples
July 2019, contractor for Siemens set logic bombs to go off after a period of time to force the company to hire him to fix the resulting damage
June 2008, systems administrator at UBS used a logic bomb to try and drive down the price of the company's stock
February 2002, a logic bomb was planted by a programmer at Deutsche Morgan Grenfell
  It was discovered before it went off but took months to remove
2012, a contractor for the US Army placed a logic bomb into the payroll systems for the US Army Reserves
  His employer had lost the contract to build the system which would affect his job
Logic bombs also can be programmed into cyber-physical systems
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 31: Backdoor Examples
A systems administrator for the City of San Francisco created a hidden admin account and backdoor
  When he was fired, he used the backdoor to lock everyone out of the system
  Software and hardware manufactures often install backdoors for testing during development
  These are undocumented, not secure and often not removed after development
  Once these backdoors are known, they provide an easily breached attack surface
In 2014. SerComm, a company that assembled routers for LinkSys and Netgear was found to have installed backdoors in the routers
Borland's Interbase (versions 4 to 6) had a backdoor that allowed anyone to take full control of all the Interbase databases
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 32: Surprise Functionality
Occurs when developers reuse source code or libraries from other projects or sources
  The reused code is not vetted or inspected thoroughly
  The resulting application now has undocumented and untested functionality
  This unknown code now presents a potential exploit
  This is not a deliberate attack, but rather just sloppy programming to produce an exploitable security flaw
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 33: Securing the Codebase
Source code is an asset that needs to be secure
  Both development code and operations infrastructure code
Best practice is to use a VCS like git with audit capabilities
  Allows tracking of where all source code and subsequent changes originated
  Once code has been finalized, it is "frozen" and cannot be changed
  Only vetted code from the codebase is used in builds
Code management and access policies can be enforced to establish a chain of possession for all code
Projects should use a standard code style so that everyone can read and understand the code
Also applies to firmware and device level code and mircocode
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 34: Securing Writing the Code
Pair programming is used to improve security and code quality
  One person codes while the other reviews the code as it is written
  In addition to catching bugs, it makes malicious code insertion very difficult
  As an extra layer of security and quality, the code is reviewed by a third developer on a random basis
To prevent collusion
  The programmers paired together every day are chosen randomly
  The third programmer who acts as reviewer is chosen randomly
Exactly the same process can be done for testing, security analysis and hardware design
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 35: Reviews
All production code and other development should be subject to formal reviews (code reviews, design reviews, etc)
  Participants should include people not involved in the project, ie. fresh eyes
  Testers and security experts should be part of the review
No component is included in a product until it passes a full review
Reviews and walk-throughs find errors and possible exploits as well as potential malicious code and flaws
Reviews are done with reference to code standards, vulnerability lists and known potential problem areas
  As well as providing a standard for best practices
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 36: Development Standards
There exist best practice standards for most areas of engineering and software design
These are intended at starting points for organizations to develop their own development standards
There are secure coding standards
  These focus on how to avoid code that introduced vulnerabilities
  These are often the result of poor programming practices
  Eg. A vulnerability is introduced in Java by failing to properly handle unchecked exceptions
Industry standards for IoT, hardware and software systems codify many of the established best practices
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 37: Security Design
Security Design Security Design
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 38: Security Responsibility
Security is not the responsibility of a “security team”
Just like quality, security is everyone’s responsibility
  A security team, like a QA team, is a resource and coordinates security related concerns
At a minimum, every person in the organization should have a clear understanding of the security responsibilities of their role
  Eg, help desk should know how to identify and respond social engineering attacks
  Eg, HR should ensure every new team member has a full security orientation
The Security Team is responsible for defining a security management program and policy
  Just like the Quality Team is responsible for defining the quality management program and policy
Also includes ensuring that everyone has:
  Access to the appropriate tools for implementing security, testing and other security related tasks
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 39: Security Responsibility
A full understanding of the organizational security policies
Training to ensure that all staff know how to execute their security responsibilities
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 40: Security Responsibility
The security team is also responsible for:
  Managing security testing activities both during development and during operations
  Developing response and mitigation plans for potential security incidents
  Monitoring all possible security related incidents
    This may include ongoing data mining and analysis of event logs
  Driving responses to security incidents
    Including reporting to appropriate authorities
    Informing management
    Implementing a mitigation and response plan
  Communicating newly discovered security issues to development and operations
  Conducting security audits
Copyright © 2021 by Elephant Scale, All Rights Reserved

## Slide 41: Security Testing
Done throughout the system lifecycle
  DevSecOps assumes continuous testing
Tiger teams are testing teams designed to act like an attacker and defeat the organization’s security measures
  Also referred to as red teams
There are two types:
  Internal: these are permanent teams that already know the security measures in place
  External: these are teams that simulate attackers with no knowledge of the security except what a real attacker could figure out
External teams can often do social engineering exploits that internal teams cannot
External teams often find novel ways to exploit a system that internal teams overlook
Copyright © 2021 by Elephant Scale, All Rights Reserved